ACME performance and precision with 8 Powercapes
using HWMON/Sigrok

---
Measurement principle
Measure the time from update to update for the first probe @0x40 and verify there is always enough time to read out all registers until next sample time is due
Write trace “a” when entering update_device
Write trace “b” after completion of i2c operations
Measure time bk– ak	cost of i2c transfer
Measure time bk – bk-1	achievable sampling period
Do this for both versions of the hwmon driver

---
Test commands
Data acquisition
trace-cmd start -p nop
sigrok-cli -d baylibre-acme --samples 200 --config samplerate=${freq}
trace-cmd stop
trace-cmd extract
Possible frequency values with sigrok-cli
Libsigrok/src/hardware/baylibre-acme will set the update interval through sysfs, possible values are discrete however, resulting of the possible averaging parameter time the constant Integration Time setting of 2.2ms
Averaging values	1	4	16	64	128	512	1024
Periods (s)	0.0022	0.0088	0.0352	0.1408	0.2816	1.1264	2.2528
Freq (Hz)	454	113.63	28.41	7.1	3.55	0.887	0.443
Tested (Hz)	454	113	28	7	3
Visualization
Done with kernelshark

---
3Hz sampling
Command
sigrok-cli -d baylibre-acme --samples 200 --config samplerate=3
Results with hwmon driver v4.3
Results with hwmon driver v4.4